## Slide 1
CFAR Detection

## Slide 2: CFAR Detection
For CFAR input, currently only support non-coherent combining for integration. Output of integration is total power from all antennas in SP floating-point only!
CFAR cell averaging (CFAR-CA) and CFAR ordered statistics (CFAR-OS) are supported.
Relative detection threshold is determined from input probability of false detection (Pf). Table is from Alek’s detection documents.
Memory used
  Scratch pad size of: fft1DSize*(sizeof(float) +sizeof(int16_t)) + 100*sizeof(float)
  Relative threshold table sizes vary from canfiguration.

## Slide 3: CFAR Detection Benchmarks
C66x Benchmarks
C674x Benchmarks
1D FFTsize | 2D FFTsize | nDetObj | CFAR-CA? | CFAR-OS? | Cycles
2048 | 32 | 34 | Yes | No | 887925
2048 | 32 | 13 | No | Yes | 6999377
1024 | 32 | 20 | Yes | No | 455540
1024 | 32 | 8 | No | Yes | 3514375
512 | 64 | 19 | Yes | No | 472102
512 | 64 | 8 | No | Yes | 3547029
256 | 128 | 19 | Yes | No | 500387
256 | 128 | 8 | No | Yes | 3612285
1D FFTsize | 2D FFTsize | nDetObj | CFAR-CA? | CFAR-OS? | Cycles
2048 | 32 | 34 | Yes | No | 2203709
2048 | 32 | 13 | No | Yes | 9220029
1024 | 32 | 20 | Yes | No | 1107895
1024 | 32 | 8 | No | Yes | 4613817
512 | 64 | 19 | Yes | No | 1112807
512 | 64 | 8 | No | Yes | 4633854
256 | 128 | 19 | Yes | No | 1124594
256 | 128 | 8 | No | Yes | 4675126